## Slide 1: Digital Systems Design Term Project: CNN Accelerator Electrical and Computer Engineering Seoul National University

## Slide 2: Table of Contents
Introduction & project goals
Background
  Convolution / FC / Pooling / ReLU
Model configuration
Module-wise description
  APB, AXI-stream / Computation layers (FC, Conv, Pool)
  VDMA
System overview
Project materials
Submission
Miscellaneous

## Slide 3: Introduction & Project Goal

## Slide 4: Introduction
Deep Learning Hardware
Google TPU
NVIDIA GPU (Titan V)
FPGA (Xilinx Virtex-7)
Intel CPU (Xeon)
NPU, etc…

## Slide 5: Project Goal
Make a CNN accelerator on the FPGA board
  Only for inference; not training
  Reconfigurable (You can not change bitstream file)
Everything will be given
  Model structure
  Datasets
  Interfaces between computer and FPGA boards
  Network parameters!
Only things to do!
  Make RTL code of 3-layers
  Check functionality using the provided test dataset

## Slide 6: Project Steps
1st : Write RTL code and implement the functionality
  Make HW work!!!
2nd : Find “the optimal point” of design (by revision)
  Speed = images / second
For step 2, you need to make design decisions
  Everything is trade-off
    Resource reuse / pipelining / parallel
    HW complexity
    Etc.
  RTL implementation of the 3-layers are your only concerns

## Slide 7: Provided Materials
Dataset
  CIFAR-10 dataset
CNN python codes
  Naïve python code for your understanding on CNN
Verilog skeleton codes
Testbench & UART ipynb file
  For each module (Conv, FC, Pool)
  For the entire project

## Slide 8: NOTE
This is not a Deep Learning course
  You need to understand the algorithm first
There are too many answer for implementation
  DO NOT COPY!

## Slide 9: Background

## Slide 10: Overview of CNN Model
Convolution Neural Network
  Convolution + ReLU (activation function)
  Pooling
  FC

## Slide 11: Convolution Layer
Convolution layers extract the features of input data
Filter
  Weight matrix to multiply with feature matrix
Stride
  Stride size: How many elements for filter to jump?
Padding
  Padding is used for making the size of input and output similar or the same
After convolution, do ReLU operation, which filters out negative values
Example of convolution computation
(stride_size=1, padding=0)
The effect of padding
(left: no padding, right: zero padding)

## Slide 12: Fully-Connected (FC) Layer
FC layers classify the data
FC = Matrix-Vector multiplication
The output of the last conv(+pool) layer is a matrix form, so it is unrolled as a vector form
After FC, do ReLU operation same as the convolution layer
Structure of FC layer 1)
Operation of FC layer2)
m
Weight
Input
Bias
=
Output
]
[
1) http://needjarvis.tistory.com/182
2) https://petewarden.com/2015/04/20/why-gemm-is-at-the-heart-of-deep-learning/

## Slide 13: Pooling Layer
Option: Max pooling, min pooling, average pooling(no comp.)
Used for preventing overfitting
Window size
  Similar to filter of conv. layer (almost 2x2)
Stride size
  How many elements for window to jump?
Example of pooling computation
(window_size=2x2, stride_size=2)

## Slide 14: Appendix
What is Deep Learning?
  https://www.nature.com/articles/nature14539
For convolutional layer,
  Refer http://cs231n.github.io/convolutional-networks/#conv
For fully-connected layer,
  Refer to Lab 06 notes
  Or refer http://cs231n.github.io/convolutional-networks/#fc
For pooling layer,
  Also refer http://cs231n.github.io/convolutional-networks/#pool

## Slide 15: Model Configuration

## Slide 16: Experiment Setup
Dataset: CIFAR-10
Model architecture: revised VGG
  # of convolutional layers = 6
  # of pooling layers = 4
  # of FC layers = 3
Trained with PyTorch framework
  The default feature/weight representation in PyTorch is (out-channel, in-channel, rows, cols)
  E.g. weight matrix: (out-channel, in-channel, rows, cols)

## Slide 17: Model Structure
Input size per img
3x32x32
CONV1 (32, 3, 3, 3)
(Out-ch, In-ch, Row, Col)
MAXPOOL1
FC1 (256, 1024)
CONV2 (64, 32, 3, 3)
MAXPOOL2
CONV3 (128, 64, 3, 3)
CONV4 (128, 128, 3, 3)
MAXPOOL3
CONV5 (256, 128, 3, 3)
CONV6 (256, 256, 3, 3)
MAXPOOL4
FC2 (64, 256)
FC3 (10, 64)
(Out, In)
Label

## Slide 18: Module-wise Description

## Slide 19: APB
Abbreviation of Advanced Peripheral Bus, which is a kind of AMBA (Advanced Microcontroller Bus Architecture) protocol
We will use this protocol on our control path
If you want to know more about the APB protocol, refer to: https://www.eecs.umich.edu/courses/eecs373/labs/lab3/IHI0024C_amba_apb_protocol_spec.pdf

## Slide 20: APB
It takes part of control flow
apb_<ex>_module
PC
APB (control flow)
top_<ex>_module

## Slide 21: APB
You can read and write values to modules from the CPU
  From the CPU, you can send start signals & receive end signals
  You can set certain parameters to your module
You can read certain values from your module from the CPU
  This might be very useful for debugging!

## Slide 22: AXI-Stream
There are three kinds of AXI
  AXI (full)
    Basic version
    Uses 5 channels for data transaction between master and slave
    (Write address/control, Write data, Write response, Read address and Read data)
  AXI-Lite (already learn in the lab session)
    Light version of AXI
    Uses 5 channels for data transaction between master and slave
    But do not use burst mode or other modes
  AXI-Stream
    We will use this in the project
    Used for sending and receiving data streams
    Uses only one channel (Write data channel) for data transaction between master and slave

## Slide 23: AXI-Stream
You have to implement below signals
  Both AXI-Stream Master and Slave interface
  ACLK and ARESETn are shared with master and slave
  Other signals exist respectively (master and slave)
  For master interface, TKEEP and TUSER is used for output and it should be set to {4{1’b1}}, 1’b0

## Slide 24: AXI-Stream
AXI port list
AXI-Stream input/output |  |  | 
Input |  | Output | 
Name | Size | Name | Size
M_AXIS_TREADY | 1-bit | S_AXIS_TREADY | 1-bit
S_AXIS_TDATA | 32-bit | M_AXIS_TDATA | 32-bit
S_AXIS_TVALID | 1-bit | M_AXIS_TVALID | 1-bit
S_AXIS_TLAST | 1-bit | M_AXIS_TLAST | 1-bit
S_AXIS_TKEEP | 4-bit | M_AXIS_TKEEP | 4-bit
S_AXIS_TUSER | 1-bit | M_AXIS_TUSER | 1-bit
AXIS_ACLK | 1-bit |  | 
AXIS_ARESETN | 1-bit |  | 

## Slide 25: AXI-Stream
When Slave is ready for get data, TREADY <= HIGH

## Slide 26: AXI-Stream
When master sends TDATA, TVALID <= HIGH

## Slide 27: AXI-stream
When TREDAY AND TVALID are both HIGH, data are sent
Send D0

## Slide 28: AXI-stream
When the last data is sent, the TLAST goes high
Send D3 (Last)

## Slide 29: AXI-Stream
After the last data is sent, TVALID and TLAST goes LOW

## Slide 30: AXI-Stream
TVALID (0) && TREADY (1) : No data sent from master
TVALID (1) && TREADY (0) : No data received from slave, master holds current data value

## Slide 31: AXI-Stream
If you want to know more information, you can make AXI-stream example file with the way you make the AXI-Lite example file. (Please refer the Lab 09)
Or you can refer the following site: https://www.xilinx.com/support/documentation/ip_documentation/ug761_axi_reference_guide.pdf

## Slide 32: FC Module
Module
  Control
  MAC (input format: 8-bit 2’s fixed-point)
  AXI-stream
Ports
  APB signal
  AXI-stream

## Slide 33: FC Module
AXI-Stream
  I/O ports are given
  Unnecessary pins are fixed to default
S_AXI: receive the data
M_AXI: send the data
The AXIS protocol ports for sending data
  m_axis_tdata, maxis_tlast, m_axis_tvalid
The AXIS protocol port for receiving data:
  s_axis_tready

## Slide 34: FC Module
APB I/O Ports
  fc_start
    PC to FPGA, Use APB protocol
    Trigger the start of operation of module’s
    When PC receive fc_done, PC set fc_start to zero
  max_index
    Check whether this fc module is last or not
    If it is last, it sends the maximum score’s index (0 to 9, =class number)
    It reduces the communication overhead of inference
  fc_done
    The port indicating that the operation of the fc layer has ended
    PC reads this value and then progresses
    fc_done flag must remain zero during processing and be HIGH when processing is over
You have to add these ports!!

## Slide 35: FC Module
top_simulation
fc_module
AXI-Stream (Data flow)
wire (control flow)
tb
Testbench structure

## Slide 36: FC Module
fc_top
fc_module
fc_apb
AXI-Stream (Data flow)
APB (Control flow)
PC
MEM
Hardware structure

## Slide 37: Conv Module
Module
  Control
  Systolic Array
    PE (=MAC) (input format: 8-bit 2’s fixed point)
  AXI-stream
Port
  APB signal
  AXI-stream

## Slide 38: Conv Module
AXI-Stream
  I/O ports are given
  Unnecessary pins are fixed to default
S_AXI: receive the data
M_AXI: send the data
The AXIS protocol ports for sending data
  m_axis_tdata, m_axis_tlast, m_axis_tvalid
The AXIS protocol port for receiving data:
  s_axis_tready

## Slide 39: Conv Module
I/O Ports
  conv_start
    PC to FPGA, Use APB protocol
    Trigger the start of operation of module’s
    When PC receive the conv_done, PC set conv_start to zero
  conv_done
    The port indicating that the operation of the conv layer has ended
    PC reads this value and then progresses.
    conv_done flag must remain zero during processing and be HIGH when processing is over

## Slide 40: Conv Module
top_simulation
conv_module
AXI-Stream (Data flow)
wire (control flow)
tb
Testbench structure

## Slide 41: Conv Module
top_conv
conv_module
conv_apb
AXI-Stream (Data flow)
APB (control flow)
PC
DRAM
Hardware structure

## Slide 42: Pooling Module
Algorithm
  max-out
Max pooling - should store each pooling’s coverage
Should store the previous row’s data

## Slide 43: Pooling Module
AXI-Stream
  I/O ports are given
  Unnecessary pins are fixed to default
S_AXI: receive the data
M_AXI: send the data
The AXIS protocol ports for sending data
  m_axis_tdata, m_axis_tlast, m_axis_tvalid
The AXIS protocol port for receiving data:
  s_axis_tready

## Slide 44: Pooling Module
I/O Ports
  pool_start
    PC to FPGA, Use APB protocol
    Trigger the start of operation of module’s
    When PC receives the pool_done, PC sets pool_start to zero
  pool_done
    The port indicating that the operation of the pool layer has ended
    PC reads this value and then progresses.
    pool_done flag must remain zero during processing and be HIGH when processing is over

## Slide 45: Pooling Module
top_simulation
pool_module
AXI-Stream (Data flow)
wire (control flow)
tb
Testbench structure

## Slide 46: Pooling Module
pool_top
pool_module
pool_apb
AXI-Stream (Data flow)
APB (control flow)
PC
DRAM

## Slide 47: ReLU Module
Activation layer (ReLU)
It is so simple
  ReLU computation is done at the last step of conv / FC module
  There is no separate module for ReLU

## Slide 48: VDMA
AXI VDMA (Video Direct Memory Access)
  Provides a high bandwidth solution for video applications
  Provides high performance direct memory access btw system memory and AXI4-Stream type target peripherals
DMA? (Direct Memory Access)
  A feature of computer systems that allows certain hardware subsystems to access main system memory independent of the CPU (Central Processing Unit) <-> (PIO)

## Slide 49: VDMA
After registers are programmed through the AXI4-Lite interfaces, the Control/Status logic block generates appropriate commands to the DataMover to initiate Write and Read commands on the AXI4 Master interface
AXI VDMA Block Diagram
Memory
FC module
S

## Slide 50: VDMA
A configurable asynchronous Line Buffer is used to temporarily hold the pixel data prior to writing it out to the AXI4-Memory Map interface or the AXI4-Stream interface.
AXI VDMA Block Diagram
Memory
FC module
S

## Slide 51: VDMA
In the Write path, the AXI VDMA accepts frames on the AXI4 Stream slave interface and writes it to system memory using the AXI4 Master interface (S2MM)
FC module
AXI VDMA Block Diagram
Stream to Memory Map (S2MM)
Memory Map to Stream (MM2S)
Memory
M
S
S
M
M

## Slide 52: VDMA
In the Read path, the AXI VDMA uses the AXI4 Master interface for reading frames from system memory and outputs it on the AXI4 Stream Master interface (M2SS)
FC module
AXI VDMA Block Diagram
Stream to Memory Map (S2MM)
Memory Map to Stream (MM2S)
Memory
M
S
S
M
M

## Slide 53: VDMA
Within the VDMA, there are registers responsible for setting the control, start address, class, hsize and vsize by data transfer direction (MM2S and S2MM)
To send data over VDMA, the values must be written to VDMA internal registers via the AXI4-Lite interface
Because it is Video DMA, default transfer unit is frame
  The frame consists of lines, and you can send data by setting the hsize (line size) and vsize (# of lines)

## Slide 54: VDMA
To operate the VDMA, write the values on the registers in the order as below
VDMACR (control) register: Setting the control (MM2S or S2MM)
START_ADDRESS register: Setting the memory address to start send or receive data
FRMDLY_STRIDE register: Setting the stride (if there is no need for using stride, set same as HSIZE
HSIZE register: Setting the HSIZE (line size in Bytes)
VSIZE register: Setting the VSIZE (# of lines)
  After setting the VSIZE, data transfer will be start on VDMA

## Slide 55: VDMA
Register address offset:
  You should only send the address value in 9-bits (b/c port width is 9-bit)
Register type | Address Offset | 
 | MM2S | S2MM
VDMACR (control) | 0x00 | 0x30
START_ADDRESS | 0x5C | 0xAC
FRMDLY_STRIDE | 0x58 | 0xA8
HSIZE | 0x54 | 0xA4
VSIZE | 0x50 | 0xA0

## Slide 56: System Overview

## Slide 57: System Overview
CNN accel. system overview
Interconnect
PC
FPGA Board
UART
UART
Module
MIG(Memory Interface Generator)
DRAM
AXI-Lite
FC Layer
CONV Layer
POOL Layer
AXI Full
AXI Stream
AXI Stream
AXI Stream

## Slide 58: System Overview
CNN accel. system overview
Interconnect
PC
FPGA Board
UART
Decoder
AXI-Lite
FC Layer
CONV Layer
POOL Layer
APB
APB
APB
MIG(Memory Interface Generator)
DRAM

## Slide 59: System Overview

## Slide 60: Memory Map
Major modules are assigned to a memory address
  DRAM : 0x0000_0000 ~ 0x0800_0000
  VDMA0 : 0x0C00_0000 ~ 0x0C10_0000
  VDMA1 : 0x0C10_0000 ~ 0x0C20_0000
  VDMA2 : 0x0C20_0000 ~ 0x0C30_0000
  APB0 : 0x0D00_0000 ~ 0x0D10_0000
  APB1 : 0x0D10_0000 ~ 0x0D20_0000
  APB2 : 0x0D20_0000 ~ 0x0D30_0000
Instructions sent from PC via UART are decoded by the decoder
  [63:60] = opcode (read: 5, write: 4)
  [59:32] = address
  [31:00] = data
Intermediate interconnects send data to the proper address
  Splitter
  Control path
  Data path

## Slide 61: Data Save
e.g., Instruction 1
Opcode = 0x04 (write)
Address = 0x0200_0000
Data = save weight or bias, etc,..
Send data to data because address is smaller than 0x0C00_0000

## Slide 62: Result Read
e.g., Instruction 2
Opcode = 0x05 (read)
Address = 0x0600_0000
Data = 0x0000_0000
Redirected to datapath and data read because the address is smaller than 0x0C00_0000

## Slide 63: PC to VDMA0
e.g., Instruction 3
Opcode = 0x04 (write)
Address = 0x0C00_0054
Data = HSIZE
Data sent to control path because the address is larger than
0x0C00_0000
Addr redirected to 0x54
Save HSIZE to VMDA’s reg

## Slide 64: VDMA0 to FC Layer
Instruction
Opcode = 0x04 (write)
Address = 0x0D00_0001
Data = apb_command
Data sent to control path because the address is larger than
0x0C00_0000
Data sent to APB0 because the address is larger than
0x0D00_0000

## Slide 65: Project Materials

## Slide 66: Provided Materials
Verilog source code
Vivado project directories referencing the above verilog source codes
Python scripts
Documentation about this project (this PPT)
Extra explanations about each materials is in the README.md file in the github repository

## Slide 67: Recommendations
You should understand how the python code works
  Look closely into scale_uart.py
    The python code interacts with the APB module (which is the control for your modules)
    Read the code & comments carefully
You should understand how to control the module
  Look closely into APB module and protocol
    You should implement your own APB module for each layer
You should understand the specifications of each layer
  Look closely what conv, fc, and pool layer does
    You should implement your own modules for each layer
  Look closely into the input/output specification of each modules

## Slide 68: Desired Roadmap
1st Week (Nov. 21th ~ Nov. 25th)
  Read the project description/code
  Share your idea with teammates
  Design the module (roughly)
2nd Week (Nov. 26th ~ Dec. 2nd)
  Implement each part
3rd Week (Dec. 3rd ~ Dec. 9th)
  Debug each part
4th Week (Dec. 10th ~ Dec. 16th)
  Extra implement and debugging (final)

## Slide 69: Submission

## Slide 70: Submission Deadline
Submission deadline:
  TBA
Checkpoint:
  Your functionality (demo)
  Evaluation time

## Slide 71: Submission Deadline
Submit to github
  Bitstream file
  Your python code (which may be revised for your design)
  Your code
  Push everything in the “main” branch of the github repository
  The final commit before the deadline will be assessed

## Slide 72: Submission Deadline
Submit to etl
  One report for each team
  One demo video for each team
    Video of running the ipynb files
    Less than 500MB
  One member should upload all the materials
We will re-check your project demo after class for rechecking and evaluating the latency criteria

## Slide 73: Report
Report deadline:
  TBA
In the report, you must include:
  Summary of the code that your team implemented
    If you haven’t finished the project, explain what your team implemented and to what level did your team succeed
    E.g., We implemented the FC layer and it passes the simulation & single_layer_test.ipynb
  Diagram of your team’s overall design
  Each members contribution (which layers did each of you designed)
Please submit on time
  “Delayed submission will be not accepted!”

## Slide 74: Miscellaneous

## Slide 75: Tips for Design
Debugging Verilog is very difficult
  It is time consuming
Synthesis and Implementation is time consuming
  Maybe…… = 1-hours in most notebook
  So, maybe most of your time is consumed in this progress

## Slide 76: Tips for Design
First, design roughly for focusing on functionality (CNN)
  Implementation can be difficult enough.
Then optimize!
Almost everything we need to do in the project has already been covered in class and lab session.
  UART
  AXI
  FC (Advanced Compute units)
But you also need to revise and implement existing/new things
  Convolutional layer
  Max-pool
  Memory-mapped

## Slide 77: Tips for Design
Before writing code of modules, plan the algorithms
  Bit operations, convolving sequences, what to store and reuse (weights or input features)
There is few designs achieving both efficiency and easiness
  So, work hard and design thoroughly!
Debugging Verilog code is very and more difficult than SW
  Everyone knows that debugging is twice as hard as writing a program in the first place. So, if you're as clever as you can be when you write it, how will you ever debug it?
  "The Elements of Programming Style", By Brian Karnighan

## Slide 78: Python API
You will use PC <-> FPGA board communication via UART
We will provide python API for you
  You do not have to modify any python codes for this project, unless if you want to modify the python codes for debugging
And reuse the environment setting in Lab08
  Use Conda to install packages!!
  Package requirements (jupyter, pyserial, numpy, matplotlib, torch, glob2)
  $ conda install pip
  $ pip install -r requirements.txt

## Slide 79: Python API
Here is the python APIs list and specifications
There are implementation details on project *.py code
First, we recommend you run the cifar_pytorch.ipynb jupyter-notebook to understand how each layer works

## Slide 80: Python API
layers_cifar10.py

## Slide 81: Python API
layers_cifar10.py

## Slide 82: Python API
layers_cifar10.py

## Slide 83: Python API
bit_operation.py

## Slide 84: Python API
setup_cifar10.py

## Slide 85: Python API
scale_uart.py
  su_set_*() functions:
  Read from file
  Write to DRAM with base address
See the scale_uart.py and all_layer_test.ipynb

## Slide 86: Python API
scale_uart.py
  You can check the address or send the val to address by this function

## Slide 87: Q&A